## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 13: Control Systems
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
Block diagrams
Properties of Laplace transforms
Building more complex systems

## Slide 3: Notes
Consider creating control systems as we go so get noise and disturbances.

## Slide 4: System Abstraction for Reaction Networks
Signal (S1, S2)
What: continuous valued function of time
Example: floating species
Single Input Single Output (SISO) System (, ))
What: transforms input signal into output signal
Example: reactions
S1
S2
J1
S3
Reaction Network
System abstraction of reaction network
J1: S1 S2; k1*S1
J2: S2 -> S3; k2*S2
S1
S2
S3

## Slide 5: Block Diagrams
Rules for drawing block diagrams
Arrows are directional signals
  May be labelled with the name of the signal
Boxes are SISO (single input single output) systems
  Internal label is the transfer function
  External label (if any) is the name of the system
Filled circles are connectors that add signals
Changing System Behavior With Control
S1
S2
S3
+
Reference: R3
Controller
Can derive the transfer function of the composed system from the block diagram.

## Slide 6: Properties of Laplace Transforms
Constant multiplication
Derivative
Integral
Summation (Systems in parallel)
is a linear operator.
These properties are used to construct the Laplace transform of a complex system.
Notes: How do the last 3 LT relate to each other?

## Slide 7: Convolution of a Signal With a System
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 0
1 | 0
2 | 0
0 | 0
1 | 0
2 | 0
Input History
Operation (Convolution)
Put input in history
Calculate output
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 0
2 | 0
0 | 10
1 | 0
2 | 0
Input History
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
Input History
0 | 10
1 | 6
2 | 0
0 | 10
1 | 6
2 | 0
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 6
2 | 5
0 | 10
1 | 6
2 | 5
Input History
+

## Slide 8: Systems in Series
Convolution definition
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 6
2 | 5
0 | 10
1 | 6
2 | 5
Input History
S1
S2
S3
Systems/signals in series are a convolution.
Convolution Laplace Transform

## Slide 9: Feedback Control System
+
Controller
Reference
Input
System
Under
Control
Measured
Output
Control
Error
Control
Input
We will use this terminology and notation.

## Slide 10: Calculating Transfer Functions In Diagrams
+
Controller
Reference
Input
System
Under
Control
Measured
Output
Control
Error
Control
Input
From the diagram
Solve for Y(s) in terms of R(s)

## Slide 11: Calculating Transfer Functions In Diagrams-1
+
Controller
Reference
Input
System
Under
Control
Measured
Output
Control
Error
Control
Input
From the diagram
Solve for Y(s) in terms of R(s)
Compare with
Notes: E(s)/R(s) + Y(s)/R(s) = 1
So, H(s) = 1 iff E(s)/R(s) = 0

## Slide 12: Application of Analysis
S1
S2
S3
+
R3
Controller
E
What are the poles of
What are the poles of
What is the DC gain of

## Slide 13: Measurement Noise
+
+
?
Measurement
Noise
From the diagram
Solve for Y(s) in terms of R(s)
If
When a system has multiple inputs, only one is non-zero in the transfer function.
Notes: TF for E/R and E/N are opposite sign.

## Slide 14: Adding a Filter
A filter smoothes noisy measurements.
+
+
Measurement
Noise
Notes: Add noise input

## Slide 15: Analysis of a More Complicated System
+

## Slide 16: Disturbances
A filter smoothes noisy measurements.
+
+
Measurement
Noise
+
Notes: Add noise input

## Slide 17: Disturbances
A disturbance perturbs how the controller actuates the system and so diminishes the effectiveness of control.
+
+
Measurement
Noise
+
Notes: Verify transfer functions

## Slide 18: BACKUP

## Slide 19: Finding
+
If , what is for a step input?
Hint:
1. What is ?
2. What is?
R
3. What is?
4. What does this tell us about the need for control action once we’re at steady state?

## Slide 20: Calcuating Transfer Functions In Diagrams
S1
S2
S3
+
R3
Controller
What is the transfer function ?
are in series, a convolution.
E
Or,
is the difference between R3 and S3.

## Slide 21: General Solution
+
Why?
+