## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 8: Laplace Transforms
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
Why Laplace Transforms?
Basic Laplace Transforms
Properties
Applying Laplace Transforms

## Slide 3: Motivating Example
How does a DC power supply convert AC power?

## Slide 4: System Abstraction for Reaction Networks
Signal (S1, S2)
What: continuous valued function of time
Example: floating species
Single Input Single Output (SISO) System (, ))
What: transforms input signal into output signal
Example: reactions
S1
S2
J1
S3
Reaction Network
System abstraction of reaction network
J1: S1 S2; k1*S1
J2: S2 -> S3; k2*S2
S1
S2
S3

## Slide 5: Operation of Linear Time Invariant (LTI) System
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 0
1 | 0
2 | 0
0 | 0
1 | 0
2 | 0
Input History
Operation (Convolution)
Put input in history
Calculate output
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 0
2 | 0
0 | 10
1 | 0
2 | 0
Input History
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
Input History
0 | 10
1 | 6
2 | 0
0 | 10
1 | 6
2 | 0
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 6
2 | 5
0 | 10
1 | 6
2 | 5
Input History
+

## Slide 6: Why Laplace Transforms (LT)
S1
S2
S3
Laplace transforms provide a mathematical description of signals and systems.
The LT for a system is called a Transfer Function.
Appeal of LT
  Describe the dynamics of a system by identifying its poles
  Calculate the step response of a system (if it converges)
  Can combine LTs of systems to infer the dynamics of the combined systems
  Important tool for control design (e.g., choosing the poles of the controlled system)

## Slide 7: LT Definition
is a complex number
is a continuous function of time
Provides a way to encode all values of as a polynomial of
  This is crucial for analyzing systems and control design

## Slide 8: A First Laplace Transform
Laplace Transform
Impulse signal at time :
Signals and systems can be described using combinations of more Laplace Transforms.
Notes: Show how can encode a discrete signal with a sum of e^-st terms. Show time shifts and scale by constant.

## Slide 9: More Laplace Transforms
Laplace Transform
Unit step at time 0: g
Ramp: g
Laplace Transform
Laplace Transform of transcendentals:

## Slide 10: What Poles Say About a System

## Slide 11: Step Response of a System
Transfer Function: The Laplace transform of a system
If a system has a unit step input (with 0 initial conditions), then its final value is .
This is also called the DC gain of the system.

## Slide 12: System Analysis Using LTs
Dynamics from poles of
Step response from

## Slide 13: Transformed Systems and Their LTs
Constant multiplication
Derivative
Integral
1
Summation
LTs are linear operators.
Notes: How do the last 3 LT relate to each other?

## Slide 14: Convolution of Transfer Functions
Convolution

## Slide 15: Inverse of a Laplace Function
General form for a T.F.:
are the zeroes, are the poles.
can be expressed as the sum of terms of that are constant multiples of .
In the time domain, these are constants, exponentials, sinusoids.
Poles indicate stability, oscillations

## Slide 16: Analysis of a Reaction Network: Calculate LTs
Finding Transfer Functions
Write state equations in terms of the inputs
Calculate the ratios for each system. Signals other than the input to and output from the system are set to 0.
Example
All reactions are mass action, and so then .
S1
S2
S3
S1
S2
S3
Notes: Possibilities for the input signal

## Slide 17: Analysis of Reaction Network: Poles and Step Response
S1
S2
S3
What is the response of to a step of size 10?
What is the response of to a step of size 10?
, then calculate final value
Notes: Possibilities for the input signal

## Slide 18: System 2: S1 is part of the system
If all reactions are mass action, then .
and so
S1
S2
S3
, since exponential decay.

## Slide 19: Analysis of System 2
S1
S2
S3

## Slide 20: BACKUP

## Slide 21: LaPlace Transform Essentials
(0 initial conditions)
Roots of D(s) are the poles of F(s)
Roots of N(s) are the zeroes of F(s)
Calculating LaPlace Transforms
Properties`
Definition