## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 6: Building Closed Loop Testbeds
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Control Architecture
Controller
+
Signals
: reference input
: control error
y: measured output
Systems
Open loop system (OLS)
Controller
Notes: Why doesn’t a filter help with measurement noise? Verify transfer functions.

## Slide 3: Open Loop System
Suppose we have an SBML model LINEAR_MDL.
import controlSBML as ctl
ctlsb = ctl.ControlSBML(LINEAR_MDL,
input_names=["S1"], output_names=["S1", "S2", "S3", "S4"])
linear_sys = ctlsb.makeNonlinearIOSystem("linear_sys")
linear_sys
linear_sys.S1
linear_sys.S1
linear_sys.S2
linear_sys.S3
linear_sys.S4
This creates a NonlinearIOSystem object linear_sys.

## Slide 4: PI Controller
controller = control.NonlinearIOSystem(
updfcn, # Updates state
outfcn, # Calculates the output
states=1, # States are unnamed and so must give a count
inputs=['in'],
outputs=['out'], name='controller')
controller
controller.in
controller.out
This creates a NonlinearIOSystem object controller.
r
u
Controller
+
y
Combine e(t) calculation

## Slide 5: Interconnect Connections for NonlinearIOSystem Objects
OUTLIST = ["linear_sys.S1", "linear_sys.S4", "controller.out"]
simple_closed = control.interconnect(
[linear_sys, controller], # systems
connections=[
['linear_sys.S1', 'controller.out'],
['controller.in', 'linear_sys.S4'],
],
inplist=["controller.in"],
outlist=OUTLIST,
)
controller
controller.in
controller.out
linear_sys
linear_sys.S1
linear_sys.S4
linear_sys.S1
linear_sys.S2
linear_sys.S3

## Slide 6: Wolf Closed Loop System
wolf_sys
controller
+
S5_SETPOINT
s5
at
Notes: Why doesn’t a filter help with measurement noise? Verify transfer functions.