## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 1: Course Introduction
Joseph L. Hellerstein
January 4, 2023
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
What is control engineering and why it’s important
Course overview
Control system concepts
Example of controller design

## Slide 3: Why Control Engineering?
Insulin Control
Bioreactor Control
Medical Device Control
Create a system that:
ensures that bounded inputs produce bounded outputs;
regulates its output;
tracks a desired objective;
minimizes cost, energy, potential dangers.

## Slide 4
Control theory is a branch of applied mathematics that deals with the design of control policies for actuated dynamical systems. Control engineering is a cross-discipline field which applies control theory to a wide range of systems such as industrial plants, aerospace, robotics and more.
Brian Douglas

## Slide 5: Structure of the Course
Control concepts
Testbed-based design
Linear time invariant (LTI) systems
LTI design

## Slide 6: Learning Objectives
Build testbeds for biomedical closed loop system
Testbed-based design of closed loop systems
Know basic LTI theory
  Construct Laplace Transforms; analyze poles; calculate DC gain
Use LTI theory to design closed loop systems

## Slide 7: Instructor
Joseph Hellerstein, Senior Fellow eScience Institute, Affiliate Professor CSE
  PhD in Computer Science
  Industry (30+ years): IBM Research, Microsoft, Google
    Mathematical models of distributed computing systems
  Current research
    Modeling evolution of microbial communities
    Model Engineering (tools for building biomedical models)

## Slide 8: Grading
Homework (2 assignments): 50%
Final project: 50%
  End-to-end analysis and design of a feedback control of an SBML model

## Slide 9: Submitting Homework
Create your folder here. Only you and the instructors have permissions for the folder.
Upload your assignment to the folder before the due date.

## Slide 10: Resources
Python
  Python programming
  Python Data Science Handbook
  Python for control engineering (Part VIII)
Control Engineering
  Modern Control Engineering, Ogata
  Linear Systems - Theory and Design, Chi-Tsong Chen
  State Space Design (YouTube), Jake Abbott (University of Utah)
  YouTube playlist for control engineering
  Steve Brunton Control Boot Camp
  Control Systems Design Online

## Slide 11: Software
The class will feature in-class exercises, so please bring a laptop to class
Software: Tellurium (http://tellurium.analogmachine.org/)
For detailed installation instructions see https://github.com/sys-bio/tellurium#installation-instructions
For a huge database of curated models see:
https://www.ebi.ac.uk/biomodels/
Other packages
  control – CalTech package for control systems design
  controlSBML – Control design with SBML models

## Slide 12: Getting Google Colaboratory (Colab)
We will use Google Colab for in-class presentation and student homeworks.
Actions: Set up Colab now on your Google Account.

## Slide 13: Introduction to Closed Loop Systems

## Slide 14: Signals & Systems
Signal
  a time series
System
  Transforms one signal(s) into another signal(s)
1 | 0.2
2 | 0.4
3 | 0.8
4 | 1.6
1 | 0.2
2 | 0.4
3 | 0.8
4 | 1.6
 | y
1 | 0.2
2 | 0.6
3 | 1.2
4 | 2.4
1 | 0.2
2 | 0.6
3 | 1.2
4 | 2.4
1 | 0.2
2 | 0.4
3 | 0.8
4 | 1.6
1 | 0.2
2 | 0.4
3 | 0.8
4 | 1.6

## Slide 15: Open Loop System (OLS)
A system/process we are given
  Has measured outputs we want to control
    Ex: blood glucose
  Has control inputs that influence the measured output
    Ex: insulin
OLS
Control inputs
Measured outputs

## Slide 16: An Example: mTOR Signaling

## Slide 17: BioChemical OLS
States: Concentrations of floating chemical species
Inputs: Changes in species concentrations
Outputs: Concentrations of floating chemical species, reaction fluxes
  Must either be a state or computable from the states (e.g., conserved species, assignment statements)
IR, IRS, Akt,
DEPTOR, mTORC1
pmTORC1, J7
Inputs (u)
States (x)
Outputs (y)
pIRS,
Akt

## Slide 18: Simple Closed Loop System
+
r
Signals
: reference input
: control error
: measured output
Systems
Open loop system
Controller
Notes: Why doesn’t a filter help with measurement noise? Verify transfer functions.

## Slide 19: CLS With Disturbances and Noise
Controller
+
+
Measurement
Noise
+
Actuator
Disturbance
Signals
: reference input
: control error
: measured output
Actuator disturbance
Measurement Noise
Systems
Open loop system
Controller
Filter
Notes: Why doesn’t a filter help with measurement noise? Verify transfer functions.

## Slide 20: Control Engineering
Given an open loop system
Achieve control objectives:
  Stable
  Has fast response
  Has measured output equal to the reference input
+
r

## Slide 21: Challenges in Control Engineering of Biological Systems
Homeostasis is not our friend.
Often need control inputs that target individual reactions.
Difficult to accurately model biological systems.

## Slide 22: Exploring Feedback Control
System identification
Design for regulation
  Effect of kP on stability, oscillations
  Bias
  Removing bias by adjusting the reference