## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Other Topics in Closed Loop Systems
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Control Design in the Frequency Domain
Frequency response
Frequency-domain control criteria
Frequency-domain control design

## Slide 3: Frequency Response
System
y
A sinusoid input to a linear system outputs a sinusoid at the same frequency but with changes in amplitude and phase.

## Slide 4: Bode Plot
A bode plot shows the response of a linear system to many frequencies of sinusoids (x-axis).
  Amplitude response (top plot)
  Phase lag (bottom plot)
amplitude
phase
The slope of the plots changes at “corner” frequencies that correspond to poles and zeros in the transfer function of the linear system.

## Slide 5: Why Bode Plots for Control Design?
Eliminating noise in control is equivalent to a low-pass filer.
Control design creates a desired low-pass filter.

## Slide 6: State Space Systems, SISO, MIMO
input
output
System
state
Single Input Single Output (SISO)
are scalars
Multiple Input Multiple Output (MIMO)
are vectors (possibly with different lengths)
Transfer Function:
Can be a matrix for a MIMO system.

## Slide 7: Examples of Closed Loop Systems
SISO Full State Feedback
X
+
SISO PID Design
input
output
System
state
Notes: Note that X(s) is a vector

## Slide 8: Controllability
Defn: The system can be driven into any state in finite time by some combination of inputs.
S0 -> S1; k0*S0
If S0 is the input and S1 is the state, are there values of S0 so that we obtain arbitrary values of S1?
If S0 is the input and S1, S2 are the states, are there values of S0 so that we obtain arbitrary values of S2, S3?
input
output
System
state
S0 -> S1; k0*S0
S1 -> S2; k1*S1

## Slide 9: Tests for Controllability
Controllability matrix has rank n.
PBH Test
has rank n.
input
output
System
state
Degree of controllability
Gramian

## Slide 10: Observability
input
output
System
state
Defn: Can estimate state from a time history of outputs.
is observable iff is controllable. So, we can use controllability results to determine observability.

## Slide 11: Optimal Control
Which controller design is best?
Optimal control
Define a cost function such that the lowest cost policy is “best”.
Controller has an optimizer that finds the lowest cost policy.

## Slide 12: Design of An Optimal Controller
+
Controller
+
Model
Optimizer
PID Controller
Optimal Controller

## Slide 13: Model Predictive Control (MPC)
MPC adds to optimal control
Prediction over a short time horizon
Model updates
Recalculation of optimizations

## Slide 14: State Observers
What do you do if you want to do full state feedback but you don’t have the full state?
input
output
System
state
State observers are feedbacks that estimate unknown internal state assuming an accurate linear model of the system.

## Slide 15: Adaptive Control
What if the model of the system changes over time?
input
output
System
state
Adaptive control provides a way to dynamically update the model of the system by comparing predictive outputs with actual outputs.

## Slide 16: Summary
Frequency design
Controllability
Observability
Optimal control
Model predictive control
State Observers
Adaptive control
Notes: Survey of Closed Loop Systems. Optimal control. Model predictive control. Controllability. Observability. Observers. Adaptive control. Fuzzy control.