## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Linear Time Invariant Systems
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
Linear time invariant (LTI) systems
Discrete time analysis
Laplace transforms
  Definition, calculation, poles
  Solving high order approximations
Poles determine stability and oscillations.
Definition of transfer function.
Calculating DC gain.

## Slide 3: The Problem
Most control properties are dynamic: stability, oscillations, settling times.
We need a way to easily assess these properties and to manipulate signals and systems (which are dynamical objects).

## Slide 4: G.P.E. Box (Famous Statistician)
All models are wrong.
But some models are useful.

## Slide 5: Modeling Signals & Systems
We want a mathematical representation of the relationship between the input signal (u) and the output signal (y).
Properties of interest
  Stability
  Setting times
  DC Gain (”final” value of y for a unit step of u)
  Oscillations
System

## Slide 6: Discrete vs. Continuous Time
System

## Slide 7: What Models?
We will mostly work with continuous time, but we start with discrete time because it’s more intuitive.
Linear discrete time model (autoregressive time series)
Linear continuous time model (differential equation)

## Slide 8: Representing Signals in Discrete Time
1
0
2
4
3
5
0
10
20
30
X
X
X
X
X
X
Let be a complex number. We can encode discrete times as a polynomial, where the exponent indicates the time index. This is called a z-transform.
k | 0 | 1 | 2 | 3 | 4 | 5
y | 5 | 10.1 | 20.03 | 15 | 30 | 11.11

## Slide 9: Shifting in time
Let the z-transform of , delayed by one time unit
k | 0 | 1 | 2 | 3 | 4 | 5
y | 5 | 10.1 | 20.03 | 15 | 30 | 11.11
k | 0 | 1 | 2 | 3 | 4 | 5
y | 10.1 | 20.03 | 15 | 30 | 11.11 | 0
original
shift
Let the z-transform of shifted by one time unit
k | 0 | 1 | 2 | 3 | 4 | 5
y | 0 | 5 | 10.1 | 20.03 | 15 | 30
delay

## Slide 10: Adding Signals
The z-transform of the sum of two time series is the sum of the z-transforms.

## Slide 11: Multiplication by a Constant
The z-transform of the product of a constant times a time series is the constant times the z-transform of the time series.

## Slide 12: Exercise: Find the z-Transform
A. Find the z-transform of
B. For which values of a is this signal bounded (stable)?
Answer:
Answer:
C. Does the signal converge faster when or when ?
Answer:

## Slide 13: From Discrete to Continuous Time
When is bounded? How does this relate to when is bounded?

## Slide 14: First Order Linear Time Invariant (LTI) System
Differential equation: ,
This system generates a signal
Solving the differential equation
  Guess : ; so,
  Substitute the guess into the differential equation.
    the characteristic equation.
  Solve the characteristic equation. The solutions are the poles.
    ;
X
c is found using the initial conditions.

## Slide 15: Poles
The poles are solutions to the characteristic equation.
What happens to when is:
  negative
  positive
  Zero
X

## Slide 16: High Order Differential Equations
  real coefficients
  n initial conditions
Solution:
  are the poles of this equation
What happens to when an is:
  negative
  positive
  zero
  imaginary
X
1st order
2nd order
3rd order
4th order

## Slide 17: Poles Tell Us About Stability and Oscillations
Consider the (possibly complex) pole
 | No oscillations | No oscillations | Unstable No oscillations
 | Transient oscillations | Persistent oscillations | Unstable oscillations
 |  |  | Unstable No oscillations
 |  |  | Unstable oscillations

## Slide 18: High Order Systems With Inputs
This is getting complicated!
We need a simpler approach than solving in the time domain.

## Slide 19: Laplace Transform
is a pure imaginary number
is a continuous function of time
The Laplace transform is closely related to the Fourier transform and is the continuous analog to the z-transform.
Provides an easy way to find poles and DC gain

## Slide 20: Basic Signals

## Slide 21: Laplace Transforms of Basic Signals
S1: , (impulse at 0)
S2: (unit step at time 0)
S3: (ramp)
S4:

## Slide 22: Laplace Transforms Properties
P1:
P2:
P3:
P4:

## Slide 23: Find These Laplace Transforms
S1:
S2:
S3:
S4:
P1:
P2:
P3:
P4:

## Slide 24: Poles & Laplace Transforms
“ is a pole of ” is equivalent to “ is a root for in the denominator of ”.
Examples

## Slide 25: What are the poles? Are the systems stable?
poles at 0. Step + impulse.
poles at -4, 0, 0.2. unstable.
S1:
S2:
S3:
S4:
P1:
P2:
P3:
P4:

## Slide 26: Transfer Function
A transfer function is the ratio of the Laplace transform of the output to the Laplace transform of the input.
S1
S2
S3
A transfer function is a Laplace transform and so has all of its properties.

## Slide 27: Final Value Theorem (for Signals)
Examples
.
.
If and converges, then
4

## Slide 28: DC Gain For Transfer Functions
Consider the transfer function .
DC Gain is when .
Derivation of DC gain
  Recall: ,
  Given this, the output signal for a step is .
  From the final value theorem,
  if converges.

## Slide 29: Examples of Calculating DC Gain
Constant amplification.
Unadjusted exponential filter.
Adjusted filter:
DC Gain:
Notes: DC gain for constant amplification: 5
DC gain for exponential: 1/a
DC gain for filter: 1

## Slide 30: What You Need to Know
Laplace Transforms of basic signals (S1-S4)
  Impulse, step, ramp, exponential
Using properties of Laplace Transforms (P1-P4)
How stability, oscillation are determined by poles
Calculating DC gain from transfer functions.