## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 7-8: Laplace Transform Theory
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
Why Laplace Transforms?
Basic Laplace Transforms
Properties
Applying Laplace Transforms

## Slide 3: The ”System” Abstraction
How does a DC power supply convert AC power?

## Slide 4: System Abstraction for Reaction Networks
Signal (S1, S2, S3)
What: continuous valued function of time
Example: floating species
Single Input Single Output (SISO) System (, ))
What: transforms input signal into output signal
Example: reactions
S1
S2
J1
S3
Reaction Network
System abstraction of reaction network
J1: S1 S2; k1*S1
J2: S2 -> S3; k2*S2
S1
S2
S3

## Slide 5: Operation of Linear Time Invariant (LTI) System
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 0
1 | 0
2 | 0
0 | 0
1 | 0
2 | 0
Input History
Operation (Convolution)
Put input in history
Calculate output
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 0
2 | 0
0 | 10
1 | 0
2 | 0
Input History
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
Input History
0 | 10
1 | 6
2 | 0
0 | 10
1 | 6
2 | 0
0 | 1.0
1 | 0.8
2 | 0.3
0 | 1.0
1 | 0.8
2 | 0.3
Function
0 | 10
1 | 6
2 | 5
0 | 10
1 | 6
2 | 5
Input History
+

## Slide 6: We Describe Signals and Systems Using Laplace Transforms
S1
S2
S3
The LT for a system is called a Transfer Function.
Appeal
  Describe the dynamics of a system by identifying its poles
  Calculate the step response of a system (if it converges)
  Can combine LTs of systems to infer the dynamics of the combined systems
  Important tool for control design (e.g., choosing the poles of the controlled system)

## Slide 7: LT Definition
is a complex number
is a continuous function of time
Provides a way to encode all values of as a polynomial of
  This is crucial for analyzing systems and control design

## Slide 8: Impulse Signal
Impulse: Instantaneous value.
Impulse signal at time :

## Slide 9: LT of an Impulse
Laplace Transform
Signals and systems can be described using combinations of more Laplace Transforms.
Notes: Show how can encode a discrete signal with a sum of e^-st terms. Show time shifts and scale by constant.

## Slide 10: More Laplace Transforms
Laplace Transform
Unit step at time 0: g
Ramp: g
Laplace Transform
Laplace Transform of transcendentals:

## Slide 11: Transfer Function
A transfer function is the ratio of the Laplace transform of the output to the Laplace transform of the input.
S1
S2
S3

## Slide 12: An Important Property of L.T.s
The derivative of is denoted by.

## Slide 13: The Poles of a System
Poles are the roots of the denominator of the transfer function.
What are the poles of the following transfer functions?

## Slide 14: Why Poles?
Poles are the roots of the denominator of the transfer function.
What happens if there is a positive pole ()?
  Unstable since the time domain is
A pole that is complex?
  Oscillates since the time domain is a sinusoid
All poles are less than 0?
  Stable system
A small value for the largest pole?
  Converges quickly

## Slide 15: Impulse Response (IR) of a System
IR Indicates how the system responds to an initial condition.
Response
Calculating impulse response
Impulse
Q: Impulse response for the following transfer functions?
Defn: Final value of output after a unit impulse at t=0.

## Slide 16: Step Response of a System (DC Gain)
Step Input
Output Response
Calculating step response.
Defn: Final value of output after a unit step at t=0.
Q: Step response for the following transfer functions?
DC Gain indicates how the input affects the output.

## Slide 17: Interpreting DC Gain
DC Gain = 0
  The input does not affect the output
DC Gain > 0
  The output increases as the input increases
DC Gain < 0
  The output decreases as the input increases
Magnitude of DC Gain is large (small)
  Increasing the input has a large (small) effect on the output
DC Gain:

## Slide 18: Workflow for System Analysis
Calculate the the transfer function.
Calculate poles and determine whether the system is stable/unstable, oscillatory.
Calculate impulse response.
Calculate DC gain.

## Slide 19: Transfer Functions for Reaction Networks
Steps for constructing TF of a system:
Define the system in terms of its input and output.
Write the state equations.
Convert state equations to Laplace Transforms.
Solve for the output in terms of the input and calculate the ratio.
S1
S2
S3
Reaction Network
J1: S1 S2; k1*S1
J2: S2 -> ; k2*S2
3. Convert to LTs.
4. Solve for transfer functions.
2. Write state equations.
1. Define the system
Notes: Possibilities for the input signal

## Slide 20: A Second Example
S1
S2
S3
Reaction Network
J1: S1 S2; k1*S1
J2: S2 -> S3; k2*S2
3. Convert to Laplace Transforms.
2. Write state equations.
1. Define the system
Q: What is ?
4. Solve for transfer functions.
Notes: Possibilities for the input signal

## Slide 21: Poles of the System
S1
S2
S3
What are the poles of:
Notes: Possibilities for the input signal

## Slide 22: Impulse Response
S1
S2
S3
Impulse response
Response to :

## Slide 23: DC Gain (Step Response)
S1
S2
S3
Response to :
Calculating step response

## Slide 24: What You Need to Know
How to construct the state equations for a chemical network.
Solve for the Laplace transforms of the states.
Construct transfer functions for systems defined by ratios of state.
Find the poles of a system.
Find the impulse response of a system.
Find the step response of a system.

## Slide 25: BACKUP

## Slide 26: Inverse of a Laplace Function
General form for a T.F.:
are the zeroes, are the poles.
can be expressed as the sum of terms of that are constant multiples of .
In the time domain, these are constants, exponentials, sinusoids.