## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 2: Elements of Closed Loop Systems
Joseph L. Hellerstein
January 9, 2023
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Agenda
Controllers
Filters
Testbed-based control design

## Slide 3: Control Architecture
Controller
+
+
Measurement
Noise
+
Actuator
Disturbance
Signals
: reference input
: control error
: measured output
: filtered output
Actuator disturbance
Measurement Noise
Systems
Open loop system (OLS)
Controller
Filter
f
m
m
Notes: Why doesn’t a filter help with measurement noise? Verify transfer functions.

## Slide 4: Proportional, Integral, Differential (PID) Controllers
PID controllers are widely used.
3 different control mechanisms that can be used in combination
All have a single input and a single output.
All make use of the control error.
Controller
+
+
Measurement
Noise
+
Actuator
Disturbance

## Slide 5: Proportional Control
Only takes into account the current error.
Appeal
Simplicity, responds to change in current control error.
Issues
Biased since once at reference value, u(t) goes to 0.
Controller
+
+
+
-

## Slide 6: Integral Control
Considers entire history of control errors.
Appeal
Unbiased
Issues
Slow response
Controller
+
+
+
-

## Slide 7: Differential Control
Senses change in control errors.
Appeal
Fast response to changes.
Issues
Works poorly with noise.
Controller
+
+
+
-

## Slide 8: Common Controllers
+
+
P Control
PI Control
PID Control
Controller
+
+
+
-

## Slide 9: Filters
Controller
+
+
+
-
Discrete time
Continuous time state equations
Rule of thumb:
Use small kF for weak signal
Use large kF for strong signal