## Slide 1: BIOE 498 / BIOE 599 Advanced Biological Control Systems Lecture 11: System Identification
Joseph L. Hellerstein
eScience Institute, Computer Science & Engineering
Allen School of Computer Science
BioEngineering
Notes: Diverse students. Some with bio-backgrounds; some without. Some with CS background; some with very limited. Two separate courses combined because of a substantial shared curriculum.

## Slide 2: Modeling Dynamical Systems
We want a mathematical representation of the relationship between the input signal (u(t)) and the output signal (y(t)).
We can reduce the need for (and time consuming use of) testbeds if the representation predicts SOG properties.
  Stable
  Oscillates
  G
System

## Slide 3: System Identification
Constructing a transfer function for the system.
This is data driven.
  We are given experimental data and the inputs that produced these data.
  From this, we estimate a transfer function that predicts values close to the experimental data.

## Slide 4: Key Concepts
Residual
Key concepts
Experimental (observational) data – what we want to predict
Fitted curve (predicted values) – predicted from out model
Residuals = Experimental data – fitted curve

## Slide 5: Transfer Functions as Models
Given the input
This means that the model is
We can use this equation to predict from .

## Slide 6: What is A Good Model?
Experimental Data
Predictions from a good model has small deviations from the experimental data.

## Slide 7: Generalizing Model to New Data
Data 2
Which is the better model now?
A good model provides good fits to many data sets.

## Slide 8: What Residuals Tell Us About Models
Functional Bias
Likely Outlier
Heteroschodasticity

## Slide 9: Calculating Residuals
The fitting procedure will attempt to minimize the difference between the model and the data points , that is minimize:

## Slide 10: Assessing Model Quality: R2
If there is uncertainty information on the data points:
A larger R2 indicates a better model.

## Slide 11: Assessing Model Quality: Chi-Square
This equation is called the weighted chi-square sum of squares.
A small is better.

## Slide 12: Assessing Model Quality: Reduced Chi-Square
An important variant of the chi-square is the reduced chi-square:
Where N is the number of data points and P the number of parameter to be fitted. This takes into account the ‘complexity’ of the model and can be use to compare different models with the same data.

## Slide 13: Under fitting
Under fitting
More Realistic

## Slide 14: You’ve probably seen this: Someone is a bit too enthusiastic with Excel
Overfitting

## Slide 15: What is A Good Model?
Fits measurement data
Simple (e.g., few parameters)
Generalizes to new measurement data
Data 1
Data 2

## Slide 16: System Identification: Estimating Model Parameters
We want to estimate the transfer function
We are given (experimental data)
Steps
  Use initial values of to predict
  If residuals = are small, stop
  If too many iterations, stop.
  Use the residuals to determine whether to increase or decrease each and predict
  Go to (2)